The uncertainty analysis and capability verification for the high pressure pVTt gas flow facility of NIM

Chunhui Li, Lishui Cui, Chi Wang

National institute of metrology of P. R. China (NIM)

No.18, Beisanhuan Donglu, Chaoyang District, Beijing, 100013

Email(corresponding author): lich@nim.ac.cn

# Abstract

The high pressure pVTt gas flow facility was built in NIM in 2014. The pressure could be changed within (100~2500) kPa. At 1000 kPa, the maximum flow rate could be 87 m3/h, while the maximum flow rate could be 47 m3/h at 2500 kPa.

With the special designing of the three way valve, the mass cancellation was achieved for the inventory volume. The uncertainty of the pVTt facility was 0.06% (k=2), while the uncertainty of the discharge coefficient of sonic nozzle could be 0.08% (k=2). The capabilities of the pVTt gas flow facility were verified by the bilateral comparisons between NIM and PTB, and between NIM and NIST with sonic nozzles.