The comparison of low pressure gas flowrate among NIM, PTB and VNIIR

Chunhui Li, Bodo Mickan and, Ilya Isaev

National institute of metrology of P. R. China (NIM)

No.18, Beisanhuan Donglu, Chaoyang District, Beijing, 100013

Email(corresponding author): lich@nim.ac.cn

Physikalisch-Technische Bundesanstalt (PTB), Germany

Email: Bodo.Mickan@ptb.de

National Metrological Institute FGUP VNIIR, Russian Federation

Email: ilya.isaev@mail.ru

# Abstract

The comparisons of low pressure gas flow rate were conducted among NIM, PTB and VNIIR from 2013.09 to 2014.11. 5 sonic nozzles were treated as the transfer meter in the comparison.

| SN | Throat diameter | Nominal Flowrate |
| --- | --- | --- |
|  | [mm] | [m3/h] |
| 2-VNIIR | 1.905 | 2 |
| 4,5-VNIIR | 2.875 | 4.5 |
| 10-VNIIR | 4.280 | 10 |
| 25-VNIIR | 6.761 | 25 |
| 50-VNIIR | 9.559 | 50 |

The pVTt primary gas flow facility was used in NIM. The bell prover was used in PTB. The Standard facility EU-1 was used in VNIIR.

The En value was calculated to evaluate the consistent of the each facility.